## Slide 1: Case study: System optimization of FPGA-accelerated FIR application
Junning Fan
UNSW Sydney

## Slide 2: Interface protocols in HLS
The IO ports are defined with INTERFACE pragma:
  applied on each argument of the synthesised function
    Special case: port =return for the return value, as well as control signals
    E.g. #pragma INTERFACE s_axilite port=a
Generates data ports or AXI-compliant IO ports:
  ap_none/ap_vld: data port
  s_axi/s_axilite: AXI memory mapped ports
  axis: AXI-stream streaming port
  Offer different IO throughput, latency and resource overhead.

## Slide 3: Burst/Streaming vs AXI-Lite
AXI-Lite takes at least 3 clock cycles to transmit a word:
  1st Clock: Master send read request, read address
  2nd Clock: Slave presents data lines, assert read data valid
  3rd Clock: Master acknowledges the read by asserting data ready
In bursting AXI-4 or streaming AXI-Stream:
  Burst: Multiple words can be transmitted with only 1 addressing cycle
  Streaming: No memory addressing
  Much higher throughput

## Slide 4: Function-wide pipelining
PIPELINE pragma can be applied to a function body:
  Pipeline all the operations in a function body
  Same syntax as pipelining loops
  Pipelining a function unrolls all loops in the function

## Slide 5: HLS code for FIR
#define TAP_DEPTH 128
void fir(float* input, float* output, float weights[TAP_DEPTH]) {
  static float shift_reg[TAP_DEPTH] = {};
  float acc = 0;
  TDL:for(int i = TAP_DEPTH-1; i >= 1; --i) {
  shift_reg[i] = shift_reg[i-1];
  }
  shift_reg[0] = *input;
  MAC:for(int i = 0; i < TAP_DEPTH; ++i) {
  acc += shift_reg[i] * weights[i];
  }
  *output = acc;
}

## Slide 6: Default HLS implementation with AXI-Lite interface

## Slide 7: HLS pragma for baseline FIR
Implement the input port as AXI-Lite (low performance without bursting)
Implement the output port as AXI-Lite (low performance without bursting)
Implement the interface of weights memory as AXI-Lite (low performance without bursting)

## Slide 8: Pipelined HLS implementation with AXI-Lite interface

## Slide 9: HLS pragma for pipelined FIR w/o bursting IO
Pipelines the function with initialize interval of 3
Partition the array to support simultaneous read/write in the unrolled loops

## Slide 10: Pipelined HLS implementation with AXI-Stream interface

## Slide 11: HLS code for streaming,pipelining FIR
typedef struct {
  fir_type_t val;
  ap_uint<1> last;} io_type_t;
void firOptimized(hls::stream<fir_type_t>& input, hls::stream<io_type_t>& output_stream, fir_type_t weights[TAP_DEPTH]) {
    static fir_type_t shift_reg[TAP_DEPTH];
    fir_type_t acc = 0;
    shift_loop: for(int i = TAP_DEPTH-1; i >= 1; --i) {
    shift_reg[i] = shift_reg[i-1];
  }
  shift_reg[0] = input.read();
  mac_loop: for(int i = 0; i < TAP_DEPTH; ++i) {
  acc += shift_reg[i] * weights[i];
  }
  io_type_t output;
  output.val = acc;
  static ap_uint<7> counter = 0;
  if (counter++ == TAP_DEPTH-1) {
  output.last = 1;
  } else {
  output.last = 0;
  }
  output_stream.write(output);
}
Special IO data for streaming in Vivado HLS
Control signal for streaming IO type

## Slide 12: HLS pragma for pipelined FIR with streaming
AXI-stream interface

## Slide 13: Resource Utilization
 | Baseline | Pipe w/o burst | Pipe with stream
LUT | 752 | 25321 | 28425
FF | 613 | 38809 | 41534
DSP | 5 | 215 | 215
Relative throughput | 0.337 | 5.48 | 22.9

## Slide 14: Relative throughput
Chart: 
| Non-opt | Opt w/o burst | Opt with burst | Desktop SW
Relative throughput | 0.337 | 5.48 | 22.9 | 20.2

## Slide 15: Takeaway messages 1
Programmable logic implementation does NOT guarantee speed-up
Pipelined/unrolled implementation can result in very large circuit

## Slide 16: Bottleneck of each design
Types of bottleneck?
Compute-bound or IO bound?
Identify bottlenecks of each design
  Hint: compute the bandwidth needed for a design to run at full speed
Assume:
  Frequency of 160MHz

## Slide 17: Baseline HLS
Bandwidth needed:
Compute-bound

## Slide 18: Pipelined HLS with AXI-Lite
Bandwidth needed:
IO-bound

## Slide 19: Pipelined HLS with AXI-Stream
Bandwidth needed:
Sub-optimal software implementation

## Slide 20
Chart: PL vs PS executing FIR on Zynq7000
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | 8192
Optimized HLS with streaming IO | 7.6369 | 11.5347 | 15.4674 | 18.6452 | 20.8024 | 21.9724 | 22.3826 | 22.5945 | 22.7477 | 22.7457 | 22.8573 | 22.8736 | 22.8595 | 22.8714
Software on Desktop (5950X) | 21.1472 | 21.1431 | 20.3857 | 20.2489 | 20.8738 | 20.6743 | 20.7573 | 20.087 | 20.4324 | 19.5272 | 20.5227 | 20.4408 | 20.6756 | 20.2483
Optimized HLS without bursting IO | 2.6166 | 3.5458 | 4.3103 | 4.8318 | 5.1431 | 5.3149 | 5.3977 | 5.4343 | 5.4562 | 5.4671 | 5.4731 | 5.4758 | 5.4773 | 5.4779
Software Baseline on Zynq PS | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Non-optimized HLS with non-bursting IO | 0.33677 | 0.33672 | 0.33671 | 0.33669 | 0.3367 | 0.33671 | 0.33664 | 0.33657 | 0.33656 | 0.33655 | 0.33657 | 0.33655 | 0.33655 | 0.33655

## Slide 21: Takeaway messages 2
The IO interface should be chosen carefully to meet the bandwidth requirement of HLS designs
PS system (software and DDR) should be able to feed data fast enough to PL system

## Slide 22: Thank you!